## Slide 1: CIC Global 2025
Pengcheng Xin
ADE Copilot

## Slide 2: What ADE Copilot can do

## Slide 3: Assistant Chatbot
Problem to resolve
  ADE has many complex features and are related to each other.
  Traditional learning methods can no longer meet the needs
  An interactive engineering assistant based on LLM is a better choice
Traditional Learning Methods
Interactive Engineering Assistant

## Slide 4: Assistant Chatbot
How ADE Copilot solves this problem
  Implement interactive engineering assistant based on pre-trained LLM(Large Language Model) and RAG(Retrieval Enhancement Generation)

## Slide 5: Measurement Generation
Problem to resolve
  Designer need to manually edit expression according to requirements
Priority | Sim Type | Simulation Name | Simulation Description | Measurements | Corners
2 | TRAN | Functional | Verification of all functional modes | – Check diff amp and CMOS modes – Check SE vs Differential mode of operation – Effect of POC signal – Effect of RX_DQ_EN – ATB functionality - Effect of POC* signals | SS, FF, extreme VT
1 | DC | Power | Active power in all modes; leakage in disabled modes. Power is measured using a 110011 bit pattern at 533Mbps | Measure current/power for each supply Tstart | Power corners
2 | … | … | … | … | …
Heavy Manual Effort
Traditional Way
Natural Language Processing And Skill expression Generation
AI Way

## Slide 6: Measurement Generation
How ADE Copilot solves this problem
  Fine Tune Pre-trained LLM based on skill source code
ID | Instruction
1 | Returns the X value where a signal crosses the threshold Y value
2 | Computes the average of a waveform over its entire range
3 | Stores the output value from one test and passes it on to another test.
… | …
ID | Ref Method
1 | cross(v("1" ?result "tran") 2.5 1 "either" t "time" )
2 | average(v("out" ?result "tran-tran"))
3 | calcVal(“trim” “myTest”)
… | …
X
Y
ADE Copilot Training

## Slide 7: Measurement Generation
How ADE Copilot solves this problem
  Task analysis and measurement generation
ID | Requirements
1 | High pulse width at vdd/2.0 / period
2 | Measure the peak current on each supply and ensure that it meets project targets
… | …
ID | Requirements
1 | fallTime(VT("/net12") 0 nil 0 nil 10 90 nil "time" )-riseTime(VT("/net12") 0 nil 0 nil 10 90 nil "time" )
2 | ymax(IT("/M1/D"))
… | …

## Slide 8: Job Policy Optimization
Problem to resolve
  Improper setting of job policy leads to waste of resources

## Slide 9: Job Policy Optimization
How ADE Copilot solves this problem
  Fine Tune pre-trained LLM based on circuit dataset
ID | Circuit | Tran analysis stop time | Simulation points
1 | 1-stage common-source amplifier | 10s | 1000
2 | 3-stage common-source amplifier | 100s | 600
3 | common-drain amplifier | 80s | 500
… | … | … | …
ID | Netlist jobs | Simulation jobs
1 | 10 | 12
2 | 20 | 46
3 | 40 | 16
… | … | …
X
Y
Data Set
ADE Copilot training

## Slide 10: Job Policy Optimization
How ADE Copilot solves this problem
  Get the optimal settings for job policy
Schematic Design
ADE Copilot Inference
Setting Job Policy Automatically
Reasonable Allocation of Resources