## Slide 1: CIC Global 2025
Pengcheng Xin
ADE Copilot – Intelligent Optimization Engine Based On LLM

## Slide 2: Overview

## Slide 3: What’s ADE Copilot
ADE(Analog Design Environment)’s intelligent optimization engine
  Based on LLM(Large Language Model)
  Optimize user experience and improve simulation performance
ADE
Copilot

## Slide 4: Architecture

## Slide 5: Architecture
REST APIs
ADE GUI
Cadence Vector DBs
Customer Vector DBs
r DB
r DB
Retrieval
Virtuoso LLM
(Default)
Customer
LLM
Commercial
LLM
JEDAI LLM
Services
Designer in the
loop plan refinement
Designer
Controller
Testbench
Agent
SKILL Generation
Agent
Planning Agent
Doc Agent
Agents
Chat Engine
Query Router
Refinement
SKILL Checker
Planning
Execution
ADE
VSE
VXL
Customer
Documents
SKILL Code
Virtuoso
Documents
APIs
SKILL Code

## Slide 6: Fine Tuning
Images: Flaticon.com, Freepik
Virtuoso Domain Knowledge
SKILL
TXT
Chunking
Unsupervised Datasets
Document Chunks
Domain Adaptation
Updated LLM
Instruction Training
Labeled Datasets
Alignment Training
Accuracy Testing
Internal
Test Datasets
MMLU
HumanEval
Public Benchmark Datasets
…
Notes: Given the relatively small size of the Virtuoso knowledge base, we use Parameter Efficient Fine Tuning (PEFT), which trains an adapter with a small number of parameters, rather than full fine tuning, which adjusts all of the weights in the model.

## Slide 7: Retrieval Augmented Generation
Cadence Vector DBs
Virtuoso Domain Knowledge
SKILL
TXT
Customer Domain Knowledge
SKILL
TXT
Chunking
Embeddings
Document Chunks
Customer Vector DBs
Chunking
Embeddings
Document Chunks
Designer
Question
Answer
Embedding
Question Vector
Similarity
Search
Top k relevant chunks
LLM
Generation
Images: Flaticon.com, Freepik
Notes: RAG is an essential approach for improving accuracy and incorporating customer-specific domain knowledge. Although it is theoretically possible to do additional fine tuning on-site at a customer with their data, the logistics are challenging, and we do not currently expect this to be necessary.

## Slide 8: Applications
Notes: This section shows two applications that are currently under development targeting an initial release in 1H2025. By the time of CIC, we expect to develop additional applications based on customer input.

## Slide 9: What ADE Copilot can do

## Slide 10: ADE Chatbot

## Slide 11: ADE Chatbot
Problem to resolve
  ADE has many complex features and are related to each other.
  Traditional learning methods can no longer meet the needs
  An interactive engineering assistant based on LLM is a better choice
Traditional Learning Methods
Interactive Engineering Assistant

## Slide 12: ADE Chatbot
How ADE Copilot solves this problem
  Implement interactive engineering assistant based on pre-trained LLM(Large Language Model) and RAG(Retrieval Enhancement Generation)

## Slide 13: Measurement Generation

## Slide 14: Measurement Generation
Problem to resolve
  Turn the custom’s requirements into skill code measurement
Priority | Sim Type | Simulation Name | Simulation Description | Measurements | Corners
2 | TRAN | Functional | Verification of all functional modes | – Check diff amp and CMOS modes – Check SE vs Differential mode of operation – Effect of POC signal – Effect of RX_DQ_EN – ATB functionality - Effect of POC* signals | SS, FF, extreme VT
1 | DC | Power | Active power in all modes; leakage in disabled modes. Power is measured using a 110011 bit pattern at 533Mbps | Measure current/power for each supply Tstart | Power corners
2 | … | … | … | … | …
Heavy Manual Effort
Traditional Way
Natural Language Processing And Skill expression Generation
AI Way

## Slide 15: Measurement Generation
How ADE Copilot solves this problem
  Fine Tune Pre-trained LLM based on skill source code
ID | Instruction
1 | Returns the X value where a signal crosses the threshold Y value
2 | Computes the average of a waveform over its entire range
3 | Stores the output value from one test and passes it on to another test.
… | …
ID | Ref Method
1 | cross(v("1" ?result "tran") 2.5 1 "either" t "time" )
2 | average(v("out" ?result "tran-tran"))
3 | calcVal(“trim” “myTest”)
… | …
X
Y
ADE Copilot Training

## Slide 16: Measurement Generation
How ADE Copilot solves this problem
  Task analysis and measurement generation
ID | Requirements
1 | High pulse width at vdd/2.0 / period
2 | Measure the peak current on each supply and ensure that it meets project targets
… | …
ID | Measurement
1 | fallTime(VT("/net12") 0 nil 0 nil 10 90 nil "time" )-riseTime(VT("/net12") 0 nil 0 nil 10 90 nil "time" )
2 | ymax(IT("/M1/D"))
… | …

## Slide 17: Measurement Generation
Create an eye diagram for v(“output_jitter” ?result “tran-tran”)
from 200.0n to 500u with a period of 10n. Return the open width of the eye using eyeMeasurement.
Instruction
Output
eyeMeasurement(
wave_eyeDiagram(
v("output_jitter"?result "tran-tran")
200.0n
500u
10n
?autoCenter t )
?horizThreshold 0 ?startx0 40 ?starty0 0 ?xTypePercent0 "t“
?endx0 60 ?endy0 50 ?yTypePercent0 "t“
?startx1 40 ?starty1 50 ?xTypePercent1 "t“
?endx1 60 ?endy1 100 ?yTypePercent1 "t“
?noOfBins 10
?measure "width“
)
This is one example of many kinds of measurements where it is much easier for a designer to describe what they want than to figure out how to write complex SKILL code
A real case
Notes: This example is working today, and we expect to add support for a variety of measurements prior to the Virtuoso 25.1 release in mid-2025.

## Slide 18: Job Policy Optimization

## Slide 19: Job Policy Optimization
Problem to resolve
  Improper setting of job policy leads to waste of resources

## Slide 20: Job Policy Optimization
How ADE Copilot solves this problem
  Fine Tune pre-trained LLM based on circuit dataset
ID | Circuit | Tran analysis stop time | Simulation points
1 | 1-stage common-source amplifier | 10s | 1000
2 | 3-stage common-source amplifier | 100s | 600
3 | common-drain amplifier | 80s | 500
… | … | … | …
ID | Netlist jobs | Simulation jobs
1 | 10 | 12
2 | 20 | 46
3 | 40 | 16
… | … | …
X
Y
Data Set
ADE Copilot training

## Slide 21: Job Policy Optimization
How ADE Copilot solves this problem
  Get the optimal settings for job policy
Schematic Design
ADE Copilot Inference
Setting Job Policy Automatically
Reasonable Allocation of Resources

## Slide 22: Summary

## Slide 23: Summary
LLMs offer transformative capabilities in understanding and generating natural language
ADE copilot is an intelligent optimization engine based on LLM, which can assistant designer and improve simulation performance
  Simplify reusing existing designs
  Learn from a customer’s existing designs and documentation
  Apply what it learns to assist the designer and to guide automation
ADE copilot has three applications currently, the first two applications already have prototypes
  ADE Chatbot
    Answer questions interactively about how ADE works and circuit design
  Measurement Generation
    Process the custom’s natural-language-requirements and generate skill measurement
  Job Policy Optimization
    Smart to set job policy automatically to improve simulation performance
VentureBeat made with OpenAI DALL-E 3 via ChatGPT Plus